## Slide 1
PHASE 0 · EXPERIMENT DESIGN REVIEW — RESEARCH POLICY RULE 1
Zero-Shot Contextual Biasing for Whisper
Trie shallow fusion + SONAR semantic gating — no model training anywhere
Implementer Murugan Rajenthiran Reviewer TBD (Rule 2) Spec EXPERIMENT_SPEC.md v0.1 Date 2026-07-28
Requesting approval of: hypothesis · baselines · dataset & split · evaluation method · frozen experimental conditions
Notes: Phase 0 gate per the research policy: no implementation until the lead approves this specification. Deck mirrors EXPERIMENT_SPEC.md v0.1 in the repo.

## Slide 2
MOTIVATION
The problem, and this phase's question
Rare words are where Whisper fails
Names, drug names, product terms — underrepresented in training data, and exactly the words users care about most.
Contextual biasing is the standard remedy
A keyword list supplied at inference nudges beam search toward expected words (shallow fusion — no training).
Our constraint: fully zero-shot
Frozen Whisper, frozen SONAR, one fixed linear map W fitted offline. No fine-tuning anywhere in the pipeline.
Research question
Can a semantic gate make trie biasing precise — boosting keywords the utterance context supports while suppressing the rest of the list?
Audio
log-mel → frozen Whisper encoder
Beam search (frozen decoder)
one BPE token per step
+ bias term on logits
trie says WHERE · SONAR gate says HOW MUCH
Transcript
rare words recovered, others untouched
Notes: Frame the task: biasing lists are legitimate context (contact names, domain vocab). The novelty is the semantic gate; everything else is established practice.

## Slide 3
PROPOSED METHOD
One added term inside the decoding loop
boost(token) = δ + λ · max(0, cos( state · W , Ekeyword ))
δ — the trie (WHERE)
BPE-token trie over the list; 4 surface forms per word (±case × ±leading space); suffix-matched per beam per step; empty suffix = new word may start.
λ·cos — the gate (HOW MUCH)
Decoder layer-4 state, pooled → projected by W into SONAR space → cosine vs each keyword embedding. Relevant words boosted hard, distractors suppressed.
W — the bridge
Fixed 512×1024 matrix, ridge-fitted once on frozen models (validated: ≈100% held-out retrieval). The only fitted artifact; checksummed and frozen.
Clean ablation by construction: λ = 0 reduces the proposed method to trie-only exactly. Baseline and proposal differ by this one term and nothing else (Rule 1).
Notes: The formula is the whole method. Emphasize: one fitted artifact (W), everything else frozen; the lambda=0 property is what makes the comparison clean.

## Slide 4
SPECIFICATION §1
Hypotheses — primary, offline-testable, and null
H1 — primary
Semantic gating beats trie-only: keyword recall +≥5 pts absolute at equal-or-better U-WER and false alarms, on both dev splits.
Decided in Phase 4 under the pre-registered operating-point rule.
H1a — embedding side
Prompt-templated keyword embeddings (e.g. “A speech that includes ‘{kw}’”) separate in-context keywords from distractors far better than bare words.
Testable offline in minutes — no ASR decoding. Answers the lead's question #1 by measurement, and gates H1 (go/no-go: separation ≥ 0.05).
H0 — null
Gated biasing ≈ trie-only at matched operating points: the gate adds no information.
If so: documented negative result; redesign targets the embedding side, not λ.
Notes: H1a exists because exploratory data showed bare-word embeddings carry no context signal (0.028). It converts the lead's prompt suggestion into a measured decision.

## Slide 5
WHY THE SPEC LOOKS THIS WAY
Exploratory evidence behind every safeguard
Pre-Phase-0 exploratory numbers — motivation only (spec §9). Not for reporting, publication, or patent discussion.
≈100%
held-out sentence retrieval, Whisper→SONAR linear map (layer 4; prefix probe 0.29 → 1.00)
The bridge W exists — the design's riskiest assumption survived first.
0.028
oracle gate separation with bare-word embeddings (in-context vs distractor)
No signal to gate on → H1a prompt templates; go/no-go pre-check before any decoding.
0 → 0.52
recall on certified baseline failures, trie-only shallow fusion at δ=3
The trie mechanism genuinely recovers words Whisper provably lost.
0.128 → 0.700
U-WER at that same δ — unconstrained boosting vandalizes unbiased words
→ pre-registered U-WER budget, error-driven mining, boost-mechanics fixes.
Notes: Each card: measurement then consequence. The spec is not speculative — every constraint traces to a number we already measured.

## Slide 6
THE INSTRUCTIVE FAILURE
Unconstrained boosting: recall up, transcript ruined
condition | WER | U-WER | recall
A baseline | 0.167 | 0.128 | 0.000
B trie δ=3 | 0.690 | 0.700 | 0.518
C trie+gate (bare words) | 0.806 | 0.822 | 0.536
C ≈ B everywhere — exactly what the 0.028 oracle separation predicted for bare-word gating.
What the damage looks like
REF …WE ARE HUSBANDMEN AND TILLERS OF THE SOIL… OUT …he, Wea Husspundman and Tillers of the soil…
Mechanism 1 — word-start distortion field: first tokens of every list word get +δ at every word boundary. Mechanism 2 — orphaned fragments: abandoned partial matches keep their earned bonus (no revocation).
U-WER-constrained operating points (§7)
Error-driven target mining — certified headroom
Boost-mechanics V2 implemented & unit-verified (decision 6)
Notes: This failure is the spec's origin story: every safeguard in sections 3, 5, 7 exists because of this table. V2 processor (potential-based revocation, first-token asymmetry) is implemented and unit-verified — decision 6 asks whether to adopt it as P's mechanism.

## Slide 7
SPECIFICATION §2
Baselines and the proposed method
ID | method | role in the experiment
B0 | Plain Whisper beam search — no biasing | Absolute reference; source of error-driven keyword mining; Phase 1 reproduces it
B1 | Trie shallow fusion — boost δ per continuing token | The established method the proposal must beat
P | B1 + semantic gate — δ + λ·max(0, cos(state·W, E_kw)) | The novel claim; λ = 0 recovers B1 exactly (built-in ablation)
Comparability guarantees
Identical decoding for all three conditions — including KV-cache OFF everywhere (P needs full-sequence states; B0/B1 match to kill the confound found in exploratory runs).
The bias term inside one LogitsProcessor is the only permitted difference; anything else requires re-approval under Rule 1.
Two-stage tuning on TUNE shard only: pick δ* with λ=0, then λ* at δ* — B1 is never handicapped.
Notes: Stress the cache-parity fix: exploratory runs had P at use_cache=False vs baselines cached — a Rule 1 violation we caught and froze out.

## Slide 8
SPECIFICATION §3
Data & split — develop on dev, keep test untouched
LibriSpeech dev-clean + dev-other (per your instruction) · streamed, never fully downloaded · utterances > 29 s excluded and counted
TUNE 25% — δ, λ, template selection
DEVTEST 75% — development-time reporting (untouched during tuning)
Shard rule (frozen): sorted(ids) → Random(42).shuffle → first 25% = TUNE. Computed on unfiltered ID lists; SHA-256 of membership printed and matched across every notebook.
Primary: IS21 deep-biasing benchmark (Le et al., Interspeech'21)
Per-utterance rare-word lists (outside the 5k most frequent training words) + distractor variants N ∈ {100, 500, 1000}; N=100 for tuning. Dev lists rebuilt with the benchmark recipe; official test lists reserved for Phase 4 → numbers directly comparable with published deep-biasing results.
Keyword lists — secondary (headroom view)
Corpus-level error-driven lists: words B0 provably substituted/deleted, rarity-filtered, + equal distractors. Guarantees measurable headroom — text-rarity mining alone gave baseline recall 0.983 (nothing to measure).
Disclosure (spec §9): exploratory mining touched test-other → that split is quarantined for final reporting. All development now on dev splits; test-clean/test-other frozen until an approved Phase 4 run.
Notes: Decision 2 on the closing slide asks which keyword protocol is primary. The disclosure is deliberate — better we flag the burned split than an auditor.

## Slide 9
SPECIFICATION §4 & §6
Frozen configuration — what can and cannot differ
condition | frozen value (B0 = B1 = P)
Model | openai/whisper-base — HF revision pinned in artifacts
Decoding | beam 5 · deterministic · language/task pinned (en, transcribe) · no timestamps
KV cache | disabled for ALL conditions (parity with P's state capture)
Preprocessing | 16 kHz mono · identical feature extraction · ≤ 29 s filter
Evaluation | one shared normalization (lowercase [a-z' ]) · jiwer version pinned · fixed attribution rules
Seeds & shards | seed 42 everywhere · shard membership recorded + SHA-256
Calibration W | fitted once before Phase 3, checksummed, never refit (corpus = decision 3)
Allowed to differ
δ (B1, P)
λ (P only)
keyword-list contents per protocol
Anything else changing mid-experiment = re-approval under Rule 1.
Notes: This slide is the Rule 1 heart: the conditions table maps one-to-one onto the policy's 'should not be changed without approval' list.

## Slide 10
SPECIFICATION §5
Evaluation metrics — recall alone is not success
Keyword recall (primary)
Occurrence-level via jiwer word alignment: a hit only if the keyword sits in an equal chunk. No substring credit ('king' ≠ 'kingsman'); multi-word entries need contiguous alignment.
B-WER / U-WER
Errors split by reference word (biased vs unbiased); insertions by hypothesis word — the IS21 benchmark's own protocol, so results are comparable with published work. U-WER is the collateral-damage meter and the tuning constraint.
False alarms
List words inserted where the reference has none. Meaningful because every list is ~50% distractors — the population the gate must suppress.
Oracle gate separation
mean cos(kw, own-utterance embedding) − mean cos(distractor, utterances). Selects the H1a template and gates condition P (go/no-go ≥ 0.05).
All metrics per split (dev-clean, dev-other) with utterance and occurrence counts alongside every rate — differences under ~20 occurrences are treated as noise.
Notes: This answers the lead's question #2: exact correct-match definition, dataset choice, and the metrics that expose vandalism, not just recovery.

## Slide 11
SPECIFICATION §7
Pre-registered success and failure criteria
Operating-point rule (TUNE only, fixed before any eval): maximize recall subject to U-WER ≤ 1.05 × B0 and false alarms ≤ B1's at the same δ.
SUCCESS
B1 − B0 ≥ +10 recall pts and P − B1 ≥ +5 pts, constraints satisfied, on both dev splits → build toward production; scale eval.
PARTIAL / NEGATIVE
B1 works but P ≈ B1 → semantic gate ineffective at this granularity. Documented negative result, interpreted through the H1a diagnostic; embedding-side redesign next.
FAILURE
No (δ, λ) satisfies the U-WER budget → shallow fusion unsafe at these scales; boost-mechanics spec (asymmetry + revocation) becomes the next Phase 0.
Go/no-go before P ever runs: best template's oracle separation ≥ 0.05 — otherwise H1a is refuted for free and no GPU-hour is spent on gated decoding.
Notes: Pre-registration is the antidote to the dev/eval reversal we saw in exploration: 15 dev utterances said delta=3 was safe; 60 eval utterances said otherwise. Thresholds themselves are decision 4.

## Slide 12
READY TO EXECUTE ON APPROVAL
Supporting instruments are already built
Prompt-template diagnostic
phase0_prompt_template_diagnostic.ipynb
5 candidate templates scored by separation gap + ROC-AUC on both dev TUNE shards. Minutes on CPU, zero ASR decoding, audio never downloaded. Output: ranked table + decision JSON → fills spec §10.1 and the go/no-go.
Phase 1 baseline validation
phase1_baseline_validation.ipynb
Reviewer-reproducible B0: frozen config echoed to artifacts, resumable per-utterance JSONL, deterministic shards with SHA-256, published-WER sanity corridor, and a written Rule 2 verification protocol.
Calibration-corpus instruments (§10.3)
2×2 grid: {WikiText, LibriSpeech} × {silence, audio}
Audio-conditioned and text-only LibriSpeech alignment notebooks fit W variants and cross-evaluate every artifact — the corpus decision gets made by measurement, then frozen.
Also prepped for Phase 2: V1 pipeline (trie + hook + LogitsProcessor, step-trace demo cell) and the V2 boost-mechanics variant, unit-verified.
Notes: Message: approval unblocks immediate, low-risk execution — the diagnostic answers question 1 the same day.

## Slide 13
PROCESS
Where we are in the approval flow
0
Design
IN REVIEW
this review — spec v0.1
1
Baseline
READY
notebook ready; needs assigned reviewer
2
Implement
PREPPED
V1 pipeline + V2 variant prepped for code review
3
Smoke
BUILT-IN
FAST mode built into every notebook
4
Full run
AWAITS 0–3
frozen config, TUNE→DEVTEST protocol
5
Audit
CONVENTIONS SET
SHA-256 artifacts, configs, transcripts committed
Policy guarantee honored: no proposed-method implementation runs as an experiment until Phases 0 and 1 are approved.
Notes: Phases 2/3 being 'prepped' is exploratory authoring, not experiment execution — nothing reportable runs before approvals.

## Slide 14
DECISIONS REQUESTED TODAY
Seven approvals to unblock Phase 1
1
Template candidate set for H1a — selection strictly by the offline diagnostic (additions welcome)
2
Adopt IS21 biasing lists as primary validation/eval (dev via recipe, official test lists at Phase 4; N=100 default) — error-driven as secondary? test-other admissible?
3
W calibration corpus — accept measure-then-freeze via the 2×2 alignment grid (§10.3)
4
Thresholds — +5 pts margin, U-WER ≤ 1.05×, go/no-go separation ≥ 0.05
5
Defer trie group-up embedding optimization to a follow-up spec (start naive, validate first)
6
Boost mechanics — adopt V2 (first-token asymmetry + failure-arc revocation) as P's mechanism, or run as an ablation arm?
7
Assign the Rule 2 reviewer — required before Phase 1 can pass
The ask: approve EXPERIMENT_SPEC.md v0.1 (with your edits) → template diagnostic runs same-day, Phase 1 baseline starts immediately.
Notes: End on decisions, not summary. Each maps to spec section 10; minute the outcomes and update the spec to v1.0 for the audit trail.